## Slide 1
Privacy
And
Voice Screening
For Environmental Sound Identification

## Slide 2
The Privacy Problem
What if it records a voice?
High quality recordings of private conversations, taken without consent
Notes: Sensors are recording high quality audio data - what happens when someone has a conversation nearby?
The conversation is recorded & stored -> privacy issue

## Slide 3
The Contexts : Environmental Sound Identification
For Industrial Noise Management
For Environmental Management
Notes: ENvironmental sound identification - using AI/Machine learning to classify audio
Industrial applications: measure noise pollution, track vehicle movement
Environmental applications - survey bird/insect/frog populations, track human or animal movements

## Slide 4
The Solution - Pre-Screening
Raw Audio Data
Preprocessing
ML Model – Voice Yes / No
Does this contain voice data?
Yes
No
Discard data
Continue routine assessment
Notes: Use a simple ML model immediately after recording
to identify data containing voice and exclude it from further analysis

## Slide 5
Prevents sensitive data from being stored
Why our solution？
Data is screened at earliest possible point in the process
Minimal impact to the monitor’s function
Notes: [see slide]
Importantly, it’s streamlined
By focusing on only whether data is voice or non-voice, much less computation is required than standard voice recognition

## Slide 6
The Solution Details
Input data 1/3 octave, short time step (<1 s, often 125 ms)
Cache data waiting for voice screening
Cache of input data
Speech recognised
No speech recognised
Core data analysis/ML classification
Once sufficient data is cached (~5s), apply speech recognition model
Set data in cache to 0
(do not delete entry, just clear values)
Release cached data

## Slide 7
Important Goals
The rest of the system works just as well
Traceability
Low resource use
Adaptable inputs
行业PPT模板http://www.1ppt.com/hangye/
Accurate classification
Notes: Voice identification shouldn’t compromise the system’s function
Ideally work with whatever the system’s input is
Clearly record when data is excluded
Monitors are usually in remote environments - power and network connection comes at a cost
Ensure representative voice identification (vocal range, accent, language)

## Slide 8
THA
NKS